## Slide 1: Jumper Virtual Lab
Installation and first steps

## Slide 2: What is Jumper Virtual Lab?
Jumper Virtual Lab is a simulation enviroment for MicroController Units (MCUs).
It currently support two different MCU platforms:
  NUCLEO-F411RE
  Nordic nRF52 DK
Target platform for this lab!

## Slide 3: Installation
What will you need:
Python 2.7.13: (unfortunately the simulator only support the old python version).
Conda: We suggest to create a virtual enviroment with such intepreter using conda. Conda installers and documentation can be found at conda_doc.
$ conda create --name jumper-vlab python=2.7.13
$ conda activate jumper-vlab
To create a new enviroment with conda simply run in a terminal instance the following commands:
Jumper vlab
Within the conda already created enviroment simply run:
$ pip install jumper matplotlib --upgrade
Solve Macos backend: https://stackoverflow.com/questions/34977388/matplotlib-runtimeerror-python-is-not-installed-as-a-framework

## Slide 4: What you need to run simulations
An hex or bin file containing the binaries associated to the code that we want to simulate.
A python script used to guide the simulation.
A board.json file containing informations about the board used and eventual external pheriperals or sensors. The file also states the connections between the different elements.
A scenario.json file containing data generators that emulates the external environment.

## Slide 5: Hex file generation
The code is based upon the Mbed OS by ARM.
A basic example of source code can be found at https://os.mbed.com/users/matteorisso/code/time_wave/
  This is not the same code used to generate the 2 Lab workloads, it’s just an example…
IMPORTANT: the Jumper simulator does not allow to monitor if the CPU is active or inactive:
  Inactive = waiting due to a sleep() system call, waiting for an interrupt, etc.
  So, the example code toggles a GPIO pin (LED) before/after each inactive period, to “notify” the simulator of the state change.

## Slide 6: Hex file generation
The code is based upon the Mbed OS by ARM
A basic example of source code can be found at https://os.mbed.com/users/matteorisso/code/time_wave/
Source code
Click on the black triangle on the right.

## Slide 7: Hex file generation (cont’d)
The code is based upon the Mbed OS by ARM
A basic example of source code can be found at https://os.mbed.com/users/matteorisso/code/time_wave/
Source code
Click on Import into Compiler.
NB: you have to create an account

## Slide 8: Hex file generation (cont’d)
The code is based upon the Mbed OS by ARM
A basic example of source code can be found at https://os.mbed.com/users/matteorisso/code/time_wave/
Give a sensible name to the program.
Click Import

## Slide 9: Hex file generation (cont’d)
The code is based upon the Mbed OS by ARM
A basic example of source code can be found at https://os.mbed.com/users/matteorisso/code/time_wave/
From this panel you can edit and navigate files
Target platform.
Always check that is Nordic nRF51-DK
Run Compile to generate the Hex file.

## Slide 10: Simulation Python Script
Simulation library
Create simulation object
Load Hex file
On every GPIO event a callback function is called and a timestamp saved.
This is used to keep track of the activity waveform in the time_stamp list.

## Slide 11: Simulation Python Script (cont’d)
Run simulation for 4000ms
Stop simulation.
Plot activity wave.

## Slide 12: board.json and scenario.json files
Board.
Temperature and humidity sensor.
board.json
Board to sensor connection with I2C.
scenario.json
Humidity and temperature syntethic data generators